## Slide 1: Packet Pacing Essentials
Rate Limit per TCP \ UDP flow
BSDCAN | June 2016

## Slide 2: About me…
My Name: Oded Shanoon
From Israel
Working for Mellanox Technologies
  SW Manager
  3+ years with FreeBSD
Background
  B.Sc. In computer science from Tel Aviv University
  Was an officer in the IAF
  I love soccer 

## Slide 3: Agenda
Introduction
Overview
  Main flow
  Kernel suggested implementation
Design Principles
Mellanox driver highlights
  Quick overview
  A few numbers
Comments

## Slide 4: Introduction - What is Packet Pacing?
Rate limited TCP/UDP socket based connections
Feature characteristics:
  Control Max bandwidth sent
  Different rates for different flows
  Smooth and even distribution between flows
  Minimal bursts sent to the network
  Avoid congestions in the network
  Prevents TCP window resizing
Goal - Offload
  Reducing CPU overhead compared to software solutions

## Slide 5: Overview – Main Flow
User Space
Kernel
HW
App
setsockopt (RL)
Network stack
Driver
Socket
rate = x
ip_output:
if (rate != 0 || ifp != new_ifp)
ioctl()
return
tx_ring_id
mbuf
tx_ring_id
thread to create tx_ring (rate)
rate limit rings
standard rings

## Slide 6: Overview – Kernel Suggested Implementation
Rate Limit proposal in Phabricator

## Slide 7: Kernel main changes summary
socket
so_max_pacing_rate
TCP/UDP
Inp_txringid_ifp
inp_txringid_max_rate
inp_txringid
IP
Add to struct inpcb
Added to struct socket
Added to ip_output
Check if socket has rate limit value
Create/delete/modify tx rate limit ring
Embed txringid and rsstype inside mbuf
Added get/set interface
SO_MAX_PACING_RATE
IOCTL
Added IOCTLs to create/delete/modify Tx rate limits
MBUF
Added new rsstype (M_HASHTYPE_TXRTLMT)

## Slide 8: Design Principles
Socket HW resources – logically connected
  We want to enjoy HW capability for offloading
  It appears as it is first of its kind…
Interface modularity
  To simplify the solution and avoid extra logic in network stack we need ifnet in the in_pcb
  For example: Route change, VLAN, lagg
Dynamic resource allocation
  The goal is to support 100k connections and more
  We would like to avoid pre-allocating resources because:
    Big memory stamp
    Lower accuracy
    Lower flexibility
  We want to create and destroy resources during flight and thus need specific flow information (ring_id, cookie) in higher levels

## Slide 9: Mellanox Driver Highlights – quick overview
Feature support as interface capability flag  IFCAP_TXRTLMT
TX Ring per rate limited TCP flow (created upon request)
Configuration and queries via sysctl
  Manage the active rate limit values
  Query HW capabilities and limitations
  Show statistics
Upon IOCTL:
  Driver always returns immediately
  Resources creation or deletion done asynchronously
On fast path rate limited packet will be directed to matching TX Ring
  According to ring_id passed through the mbuf

## Slide 10: Mellanox Driver Highlights – a few numbers
Number of rate limited connections - up to 45,000 on ConnectX-3 or 100,000 on ConnectX-4
  Achieve line rate bandwidth with maximum connections
120 different RL values per port on ConnectX-3. Should be ~500 on ConnectX-4
Supported rates: 250Kb/s - 50Mb/s (Should expand on ConnectX-4)
Configurable burst size (Low = 3 packets, High = 5-6 packets)

## Slide 11: Comments and questions

## Slide 12
Thank You

## Slide 13: Overview – Kernel Suggested Implementation
sys/netinet/in_pcb.h:
struct inpcb {
+ struct ifnet *inp_txringid_ifp;
+ uint32_t inp_txringid_max_rate;
+ uint32_t inp_txringid;
}
sys/socketvar.h:
struct socket {
+ uint32_t so_max_pacing_rate;
}
sys/mbuf.h:
struct mbuf {
+ #define M_HASHTYPE_TXRTLMT 11
}
  sys/sys/sockio.h:
  + #define SIOCARATECTL _IOWR('i', 139, struct ifreq_txrtlmt)
  + #define SIOCSRATECTL _IOWR('i', 140, struct ifreq_txrtlmt)
  + #define SIOCDRATECTL _IOW('i', 141, struct ifreq_txrtlmt)